## Slide 1: CARTESIAN VECTORS AND THEIR ADDITION & SUBTRACTION
In-Class Activities:
Reading Quiz
Applications/Relevance
A Unit Vector
3-D Vector Terms
Adding Vectors
Concept Quiz
Examples
Attention Quiz
Today’s Objectives:
Students will be able to:
a) Represent a 3-D vector in a Cartesian coordinate system.
b) Find the magnitude and coordinate angles of a 3-D vector
c) Add vectors (forces) in 3-D space

## Slide 2: READING QUIZ
1. Vector algebra, as we are going to use it, is based on a ___________ coordinate system.
A) Euclidean B) Left-handed
C) Greek D) Right-handed E) Egyptian
2. The symbols , , and  designate the __________ of a 3-D Cartesian vector.
A) Unit vectors B) Coordinate direction angles
C) Greek societies D) X, Y and Z components
Notes: Answers:
1. D
2. B

## Slide 3: APPLICATIONS
In this case, the power pole has guy wires helping to keep it upright in high winds. How would you represent the forces in the cables using Cartesian vector form?
Many structures and machines involve 3-dimensional space.

## Slide 4: APPLICATIONS (continued)
In the case of this radio tower, if you know the forces in the three cables, how would you determine the resultant force acting at D, the top of the tower?

## Slide 5: CARTESIAN UNIT VECTORS
The unit vectors in the Cartesian axis system are i, j, and k. They are unit vectors along the positive x, y, and z axes respectively.
Characteristics of a unit vector :
a) Its magnitude is 1.
b) It is dimensionless (has no units).
c) It points in the same direction as the original vector (A).
For a vector A, with a magnitude of A, an unit vector is defined as uA = A / A .

## Slide 6: CARTESIAN VECTOR REPRESENTATION
Consider a box with sides AX, AY, and AZ meters long.
The vector A can be defined as A = (AX i + AY j + AZ k) m
The projection of vector A in the x-y plane is A´. The magnitude of A´ is found by using the same approach as a 2-D vector: A´ = (AX2 + AY2)1/2 .
The magnitude of the position vector A can now be obtained as
A = ((A´)2 + AZ2) ½ = (AX2 + AY2 + AZ2) ½

## Slide 7: DIRECTION OF A CARTESIAN VECTOR
These angles are not independent. They must satisfy the following equation.
cos²  + cos²  + cos²  = 1
This result can be derived from the definition of a coordinate direction angles and the unit vector. Recall, the formula for finding the unit vector of any position vector:
or written another way, uA = cos  i + cos  j + cos  k .
These angles are measured between the vector and the positive X, Y and Z axes, respectively. Their range of values are from 0° to 180°
The direction or orientation of vector A is defined by the angles , β, and γ.
Using trigonometry, “direction cosines” are found using

## Slide 8: ADDITION OF CARTESIAN VECTORS (Section 2.6)
For example, if
A = AX i + AY j + AZ k and
B = BX i + BY j + BZ k , then
A + B = (AX + BX) i + (AY + BY) j + (AZ + BZ) k
or
A – B = (AX - BX) i + (AY - BY) j + (AZ - BZ) k .
Once individual vectors are written in Cartesian form, it is easy to add or subtract them. The process is essentially the same as when 2-D vectors are added.

## Slide 9: IMPORTANT NOTES
Sometimes 3-D vector information is given as:
a) Magnitude and the coordinate direction angles, or,
b) Magnitude and projection angles.
You should be able to use both these sets of information to change the representation of the vector into the Cartesian form, i.e.,
F = {10 i – 20 j + 30 k} N .

## Slide 10: EXAMPLE
Using geometry and trigonometry, write F1 and F2 in Cartesian vector form.
2) Then add the two forces (by adding x and y-components).
G
Given: Two forces F1 and F2 are applied to a hook.
Find: The resultant force in Cartesian vector form.
Plan:
Notes: Source : F 2-18

## Slide 11: EXAMPLE (continued)
Fz = 500 (3/5) = 300 lb
Fx = 0 = 0 lb
Fy = 500 (4/5) = 400 lb
Now, write F1 in Cartesian vector form (don’t forget the units!).
F1 = {0 i + 400 j + 300 k} lb
Solution: First, resolve force F1.

## Slide 12: EXAMPLE (continued)
Now, resolve force F2.
F2z = -800 sin 45° =  565.7 lb
F2’ = 800 cos 45° = 565.7 lb
F2’ can be further resolved as,
F2x = 565.7 cos 30° = 489.9 lb
F2y = 565.7 sin 30° = 282.8 lb
Thus, we can write:
F2 = {489.9 i + 282.8 j  565.7 k } lb
F2’
F2z

## Slide 13: EXAMPLE (continued)
So FR = F1 + F2 and
F1 = {0 i + 400 j + 300 k} lb
F2 = {489.9 i + 282.8 j  565.7 k } lb
FR = { 490 i + 683 j  266 k } lb

## Slide 14: CONCEPT QUIZ
1. If you know only uA, you can determine the ________ of A uniquely.
A) magnitude B) angles (,  and )
C) components (AX, AY, & AZ) D) All of the above.
2. For a force vector, the following parameters are randomly generated. The magnitude is 0.9 N,  = 30º , β= 70º , γ = 100º. What is wrong with this 3-D vector ?
A) Magnitude is too small.
B) Angles are too large.
C) All three angles are arbitrarily picked.
D) All three angles are between 0º to 180º.
Notes: Answers:
1. B
2. C

## Slide 15: GROUP PROBLEM SOLVING
1) Using the geometry and trigonometry, resolve and write F1 and F2 in the Cartesian vector form.
2) Add F1 and F2 to get FR.
3) Determine the magnitude and angles , , .
Given: The screw eye is subjected to two forces, F1 and F2.
Find: The magnitude and the coordinate direction angles of the resultant force.
Plan:
Notes: Source : P2-80

## Slide 16: GROUP PROBLEM SOLVING (continued)
F´ can be further resolved as,
F1x = 204.8 sin 25° = 86.6 N
F1y = 204.8 cos 25° = 185.6 N
First resolve the force F1.
F1z = - 250 sin 35° = - 143.4 N
F´ = 250 cos 35° = 204.8 N
Now we can write:
F1 = {86.6 i + 185.6 j  143.4 k } N
F´
F1z

## Slide 17: GROUP PROBLEM SOLVING (continued)
F2 = { -200 i + 282.8 j +200 k } N
The force F2 can be represented in the Cartesian vector form as:
F2 = 400{ cos 120° i + cos 45° j + cos 60° k } N
= { -200 i + 282.8 j + 200 k } N
Now, resolve force F2.

## Slide 18: GROUP PROBLEM SOLVING (continued)
Now find the magnitude and direction angles for the vector.
FR = {(-113.4)2 + 468.42 + 56.62}1/2 = 485.2 = 485 N
 = cos-1 (FRx / FR) = cos-1 (-113.4 / 485.2) = 104°
 = cos-1 (FRy / FR) = cos-1 (468.4 / 485.2) = 15.1°
 = cos-1 (FRz / FR) = cos-1 (56.6 / 485.2) = 83.3°
So FR = F1 + F2 and
F1 = { 86.6 i + 185.6 j  143.4 k} N
F2 = { -200 i + 282.8 j + 200 k} N
FR = { -113.4 i + 468.4 j + 56.6 k} N

## Slide 19: ATTENTION QUIZ
1. What is not true about an unit vector, e.g., uA?
A) It is dimensionless.
B) Its magnitude is one.
C) It always points in the direction of positive X- axis.
D) It always points in the direction of vector A.
2. If F = {10 i + 10 j + 10 k} N and
G = {20 i + 20 j + 20 k } N, then F + G = { ____ } N
A) 10 i + 10 j + 10 k
B) 30 i + 20 j + 30 k
C) – 10 i – 10 j – 10 k
D) 30 i + 30 j + 30 k
Notes: Answers:
1. C
2. D

## Slide 20
End of the Lecture
Let Learning Continue