## Slide 1: POSITION VECTORS & FORCE VECTORS
In-Class Activities:
Check Homework
Reading Quiz
Applications / Relevance
Write Position Vectors
Write a Force Vector along a line
Concept Quiz
Group Problem
Attention Quiz
Today’s Objectives:
Students will be able to :
a) Represent a position vector in Cartesian coordinate form, from given geometry.
b) Represent a force vector directed along a line.

## Slide 2: READING QUIZ
1. The position vector rPQ is obtained by
A) Coordinates of Q minus coordinates of the origin
B) Coordinates of P minus coordinates of Q
C) Coordinates of Q minus coordinates of P
D) Coordinates of the origin minus coordinates of P
2. A force of magnitude F, directed along a unit vector U, is given by F = ______ .
A) F (U)
B) U / F
C) F / U
D) F + U
E) F – U
Notes: Answers:
1. C
2. A

## Slide 3: APPLICATIONS
This ship’s mooring line, connected to the bow, can be represented as a Cartesian vector.
What are the forces in the mooring line and how do we find their directions?
Why would we want to know these things?

## Slide 4: APPLICATIONS (continued)
This awning is held up by three chains. What are the forces in the chains and how do we find their directions? Why would we want to know these things?

## Slide 5: POSITION VECTOR
Consider two points, A and B, in 3-D space. Let their coordinates be (XA, YA, ZA) and (XB, YB, ZB), respectively.
A position vector is defined as a fixed vector that locates a point in space relative to another point.

## Slide 6: POSITION VECTOR (continued)
The position vector directed from A to B, rAB , is defined as
rAB = {( XB – XA ) i + ( YB – YA ) j + ( ZB – ZA ) k }m
Please note that B is the ending point and A is the starting point. ALWAYS subtract the “tail” coordinates from the “tip” coordinates!

## Slide 7: FORCE VECTOR DIRECTED ALONG A LINE (Section 2.8)
a) Find the position vector, rAB , along two points on that line.
b) Find the unit vector describing the line’s direction, uAB = (rAB/rAB).
c) Multiply the unit vector by the magnitude of the force, F = F uAB .
If a force is directed along a line, then we can represent the force vector in Cartesian coordinates by using a unit vector and the force’s magnitude. So we need to:

## Slide 8: EXAMPLE
Plan:
1. Find the position vector rAC and its unit vector uAC.
2. Obtain the force vector as FAC = 420 N uAC .
Given: The 420 N force along the cable AC.
Find: The force FAC in the Cartesian vector form.
Notes: Source : F2-23

## Slide 9: EXAMPLE (continued)
(We can also find rAC by subtracting the coordinates of A from the coordinates of C.)
rAC = {22 + 32 + (-6)2}1/2 = 7 m
Now uAC = rAC/rAC and FAC = 420 uAC = 420 (rAC/rAC )
So FAC = 420{ (2 i + 3 j  6 k) / 7 } N
= {120 i + 180 j  360 k } N
As per the figure, when relating A to C, we will have to go 2 m in the x-direction, 3 m in the y-direction, and -6 m in the z-direction. Hence,
rAC = {2 i + 3 j  6 k} m.

## Slide 10: CONCEPT QUIZ
1. P and Q are two points in a 3-D space. How are the position vectors rPQ and rQP related?
A) rPQ = rQP B) rPQ = - rQP
C) rPQ = 1/rQP D) rPQ = 2 rQP
2. If F and r are force and position vectors, respectively, in SI units, what are the units of the expression (r * (F / F)) ?
A) Newton B) Dimensionless
C) Meter D) Newton - Meter
E) The expression is algebraically illegal.
Notes: Answers:
1. B
2. C

## Slide 11: GROUP PROBLEM SOLVING
Plan:
1) Find the forces along AB and AC in the Cartesian vector form.
2) Add the two forces to get the resultant force, FR.
3) Determine the magnitude and the coordinate angles of FR.
Given: Two forces are acting on a flag pole as shown in the figure. FB = 560 N and FC = 700 N
Find: The magnitude and the coordinate direction angles of the resultant force.
Notes: Source : P2-94

## Slide 12: GROUP PROBLEM SOLVING (continued)
FAC = 700 (rAC / rAC) N
FAC = 700 (3 i + 2 j – 6 k) / 7 N
FAC = {300 i + 200 j – 600 k} N
FAB = 560 (rAB / rAB) N
FAB = 560 ( 2 i – 3 j – 6 k) / 7 N
FAB = (160 i – 240 j – 480 k) N
rAB = {2 i  3 j  6 k} m
rAC = {3 i + 2 j  6 k} m
rAB = {22 + (-3)2 + (-6)2}1/2 = 7 m
rAC = {32 + 22 + (-6)2}1/2 = 7 m

## Slide 13: GROUP PROBLEM SOLVING (continued)
FR = {4602 + (-40)2 + (-1080)2}1/2
= 1174.6 N
FR = 1175 N
FR = FAB + FAC
= {460 i – 40 j – 1080 k} N
 = cos-1(460/1175) = 66.9°
 = cos-1(–40/1175) = 92.0°
 = cos-1(–1080/1175) = 157°

## Slide 14: ATTENTION QUIZ
1. Two points in 3–D space have coordinates of P (1, 2, 3) and Q (4, 5, 6) meters. The position vector rQP is given by
A) {3 i + 3 j + 3 k} m
B) {– 3 i – 3 j – 3 k} m
C) {5 i + 7 j + 9 k} m
D) {– 3 i + 3 j + 3 k} m
E) {4 i + 5 j + 6 k} m
2. A force vector, F, directed along a line defined by PQ is given by
A) (F/ F) rPQ B) rPQ/rPQ
C) F(rPQ/rPQ) D) F(rPQ/rPQ)
Notes: Answers
1. B
2. C

## Slide 15
End of the Lecture
Let Learning Continue