## Slide 1: EQUILIBRIUM OF A PARTICLE, THE FREE-BODY DIAGRAM & COPLANAR FORCE SYSTEMS
In-Class Activities:
Reading Quiz
Applications
What, Why and How of a FBD
Equations of Equilibrium
Analysis of Spring and Pulleys
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objectives:
Students will be able to :
a) Draw a free body diagram (FBD), and,
b) Apply equations of equilibrium to solve a 2-D problem.

## Slide 2: READING QUIZ
1) When a particle is in equilibrium, the sum of forces acting on it equals ___ . (Choose the most appropriate answer)
A) A constant B) A positive number C) Zero
D) A negative number E) An integer
2) For a frictionless pulley and cable, tensions in the cable (T1 and T2) are related as _____ .
A) T1 > T2
B) T1 = T2
C) T1 < T2
D) T1 = T2 sin 
Notes: Answers:
1. C
2. B

## Slide 3: APPLICATIONS
The crane is lifting a load. To decide if the straps holding the load to the crane hook will fail, you need to know forces in the straps. How could you find those forces?
Straps

## Slide 4: APPLICATIONS (continued)
For a spool of given weight, how would you find the forces in cables AB and AC? If designing a spreader bar like the one being used here, you need to know the forces to make sure the rigging doesn’t fail.

## Slide 5: APPLICATIONS (continued)
For a given force exerted on the boat’s towing pendant, what are the forces in the bridle cables? What size of cable must you use?

## Slide 6: COPLANAR FORCE SYSTEMS (Section 3.3)
To determine the tensions in the cables for a given weight of cylinder, you need to learn how to draw a free-body diagram and apply the equations of equilibrium.
This is an example of a 2-D or coplanar force system.
If the whole assembly is in equilibrium, then particle A is also in equilibrium.
Notes: Explain the following terms :
Coplanar force system – The forces lie on a sheet of paper (plane).
A particle – It has a mass, but a size that can be neglected.
Equilibrium – A condition of rest or constant velocity.

## Slide 7: THE WHAT, WHY AND HOW OF A FREE BODY DIAGRAM (FBD)
Free-body diagrams are one of the most important things for you to know how to draw and use for statics and other subjects!
What? - It is a drawing that shows all external forces acting on the particle.
Why? - It is key to being able to write the equations of equilibrium—which are used to solve for the unknowns (usually forces or angles).

## Slide 8
Active forces: They want to move the particle. Reactive forces: They tend to resist the motion.
Note : Cylinder mass = 40 Kg
1. Imagine the particle to be isolated or cut free from its surroundings.
A
3. Identify each force and show all known magnitudes and directions. Show all unknown magnitudes and / or directions as variables.
FC = 392.4 N (What is this?)
FB
FD
30˚
2. Show all the forces that act on the particle.
FBD at A
A
y
x
How?
Notes: Mainly explain the three steps using the example .

## Slide 9: EQUATIONS OF 2-D EQUILIBRIUM
Or, written in a scalar form,
Fx = 0 and  Fy = 0
These are two scalar equations of equilibrium (E-of-E). They can be used to solve for up to two unknowns.
Since particle A is in equilibrium, the net force at A is zero.
So FB + FC + FD = 0
or F = 0
FBD at A
A
In general, for a particle in equilibrium,
 F = 0 or
 Fx i +  Fy j = 0 = 0 i + 0 j (a vector equation)
FBD at A
A
FB
FD
A
FC = 392.4 N
y
x
30˚

## Slide 10: EQUATIONS OF 2-D EQUILIBRIUM (continued)
Write the scalar E-of-E:
+   Fx = FB cos 30º – FD = 0
+   Fy = FB sin 30º – 392.4 N = 0
Solving the second equation gives: FB = 785 N →
From the first equation, we get: FD = 680 N ←
Note : Cylinder mass = 40 Kg
FBD at A
A
FB
FD
A
FC = 392.4 N
y
x
30˚
Notes: You may tell students that they should know how to solve linear simultaneous equations by hand and also using calculator . If they need help they can see you .

## Slide 11: SIMPLE SPRINGS
Spring Force = spring constant * deformation of spring
or F = k * s

## Slide 12: CABLES AND PULLEYS
With a frictionless pulley and cable
T1 = T2.
T1
T2
Cable can support only a tension or “pulling” force, and this force always acts in the direction of the cable.

## Slide 13: Smooth Contact
If an object rests on a smooth surface, then the surface will exert a force on the object that is normal to the surface at the point of contact.
In addition to this normal force N, the cylinder is also subjected to its weight W and the force T of the cord.
Since these three forces are concurrent at the center of the cylinder, we can apply the
equation of equilibrium to this “particle,” which is the same as applying it to the cylinder.

## Slide 14: EXAMPLE I
Plan:
1. Draw a FBD for point A.
2. Apply the E-of-E to solve for the forces in ropes AB and AC.
Given: The box weighs 550 lb and geometry is as shown.
Find: The forces in the ropes AB and AC.
Notes: Source : F3-1

## Slide 15: EXAMPLE I (continued)
FBD at point A
FC
FB
A
FD = 550 lb
y
x
30˚
3
4
5
Applying the scalar E-of-E at A, we get;
+   F x = – FB cos 30° + FC (4/5) = 0
+   F y = FB sin 30° + FC (3/5) - 550 lb = 0
Solving the above equations, we get;
FB = 478 lb and FC = 518 lb

## Slide 16: EXAMPLE II
Plan:
1. Draw a FBD for point E.
2. Apply the E-of-E to solve for the forces in cables DE, EA, and EB.
Given: The mass of cylinder C is 40 kg and geometry is as shown.
Find: The tensions in cables DE, EA, and EB.
Notes: Source : F3-5

## Slide 17: EXAMPLE II (continued)
FBD at point E
Applying the scalar E-of-E at E, we get;
+   F x =  TED + (40*9.81) cos 30° = 0
+   F y = (40*9.81) sin 30°  TEA = 0
Solving the above equations, we get;
TED = 340 N  and TEA = 196 N 
TEB = 40*9.81 N
TED
E
TEA
y
x
30˚

## Slide 18: CONCEPT QUIZ
1) Assuming you know the geometry of the ropes, in which system above can you NOT determine forces in the cables?
1000 lb
1000 lb
1000 lb
( A ) ( B ) ( C )
A) The weight is too heavy.
B) The cables are too thin.
C) There are more unknowns than equations.
D) There are too few cables for a 1000 lb weight.
2) Why?
Notes: Answers:
1. C
2. C
You may ask the students to record their answers, first, without group discussion and later after the group discussion with their neighbors. Again, like after reading quiz, they should verbally indicate the answers. You can comment on the answers, emphasizing statically indeterminate condition.

## Slide 19: GROUP PROBLEM SOLVING
1. Draw a FBD for Point D.
2. Apply E-of-E at Point D to solve for the unknowns (FCD & FDE).
3. Knowing FCD, repeat this process at point C.
Given: The mass of lamp is 20 kg and geometry is as shown.
Find: The force in each cable.
Plan:
Notes: Source : P3-29

## Slide 20: GROUP PROBLEM SOLVING (continued)
FBD at point D
FDE
FCD
D
W = 20 (9.81) N
y
x
30˚
Applying the scalar E-of-E at D, we get;
+  Fy = FDE sin 30° – 20 (9.81) = 0
+  Fx = FDE cos 30° – FCD = 0
Solving the above equations, we get:
FDE = 392 N and FCD = 340 N

## Slide 21: GROUP PROBLEM SOLVING (continued)
FBD at point C
FCD =340 N
FAC
C
y
x
45˚
FBC
3
4
5
Applying the scalar E-of-E at C, we get;
+  Fx = 340 – FBC sin 45° – FAC (3/5) = 0
+   Fy = FAC (4/5) – FBC cos 45° = 0
Solving the above equations, we get;
FBC = 275 N and FAC = 243 N

## Slide 22: ATTENTION QUIZ
A
30
40
100 lb
1. Select the correct FBD of particle A.
A)
A
100 lb
B)
30
40°
A
F1 F2
C)
30°
A
F
100 lb
A
30°
40°
F1
F2
100 lb
D)
Notes: Answers:
1. D

## Slide 23: ATTENTION QUIZ
F2
20 lb
F1
C
50°
2. Using this FBD of Point C, the sum of forces in the x-direction ( FX) is ___ . Use a sign convention of +  .
A) F2 sin 50° – 20 = 0
B) F2 cos 50° – 20 = 0
C) F2 sin 50° – F1 = 0
D) F2 cos 50° + 20 = 0
Notes: Answers:
2. B

## Slide 24
End of the Lecture
Let Learning Continue