## Slide 1: THREE-DIMENSIONAL FORCE SYSTEMS
  In-class Activities:
  Check Homework
  Reading Quiz
  Applications
  Equations of Equilibrium
  Concept Questions
  Group Problem Solving
  Attention Quiz
Today’s Objectives:
Students will be able to solve 3-D particle equilibrium problems by
a) Drawing a 3-D free body diagram, and,
b) Applying the three scalar equations (based on one vector equation) of equilibrium.

## Slide 2: READING QUIZ
1. Particle P is in equilibrium with five (5) forces acting on it in 3-D space. How many scalar equations of equilibrium can be written for point P?
A) 2 B) 3 C) 4
D) 5 E) 6
2. In 3-D, when a particle is in equilibrium, which of the following equations apply?
  A) ( Fx) i + ( Fy) j + ( Fz) k = 0
  B)  F = 0
  C)  Fx =  Fy =  Fz = 0
  D) All of the above.
  E) None of the above.
Notes: Answers:
1. B
2. D

## Slide 3: APPLICATIONS
You know the weight of the electromagnet and its load. But, you need to know the forces in the chains to see if it is a safe assembly. How would you do this?

## Slide 4: APPLICATIONS (continued)
This shear-leg derrick is to be designed to lift a maximum of 200 kg of fish.
How would you find the effect of different offset distances on the forces in the cable and derrick legs?
Offset distance

## Slide 5: THE EQUATIONS OF 3-D EQUILIBRIUM
This vector equation will be satisfied only when
Fx = 0
Fy = 0
Fz = 0
These equations are the three scalar equations of equilibrium. They are valid for any point in equilibrium and allow you to solve for up to three unknowns.
When a particle is in equilibrium, the vector sum of all the forces acting on it must be zero ( F = 0 ) .
This equation can be written in terms of its x, y and z components. This form is written as follows.
( Fx) i + ( Fy) j + ( Fz) k = 0

## Slide 6: EXAMPLE I
1) Draw a FBD of particle A.
2) Write the unknown cable forces TB, TC , and TD in Cartesian vector form.
3) Apply the three equilibrium equations to solve for the tension
in cables.
Given: The four forces and geometry shown.
Find: The tension developed in cables AB, AC, and AD.
Plan:
Notes: Source : F3-10

## Slide 7: EXAMPLE I (continued)
W = -300 k
Solution:
TB = TB i
TC =  (TC cos 60) sin30 i + (TC cos 60) cos30 j + TC sin 60 k
TC = TC (-0.25 i +0.433 j +0.866 k )
TD = TD cos 120 i + TD cos 120 j +TD cos 45 k
TD = TD ( 0.5 i  0.5 j + 0.7071 k )
TC
TD
TB
FBD at A

## Slide 8: EXAMPLE I (continued)
Equating the respective i, j, k components to zero, we have
Fx = TB – 0.25 TC – 0.5 TD = 0 (1)
Fy = 0.433 TC – 0.5 TD = 0 (2)
Fz = 0.866 TC + 0.7071 TD – 300 = 0 (3)
FR = 0 = TB i + TC ( 0.25 i +0.433 j + 0.866 k )
+ TD ( 0.5 i  0.5 j + 0.7071 k )
 300 k
Applying equilibrium equations:
Using (2) and (3), we can determine TC = 203 lb, TD = 176 lb
Substituting TC and TD into (1), we can find TB = 139 lb

## Slide 9: EXAMPLE II
1) Draw a free body diagram of Point A. Let the unknown force magnitudes be FB, FC, FD .
2) Represent each force in its Cartesian vector form.
3) Apply equilibrium equations to solve for the three unknowns.
Given: A 600 N load is supported by three cords with the geometry as shown.
Find: The tension in cords AB, AC and AD.
Plan:
Notes: Source : F3-9

## Slide 10: EXAMPLE II (continued)
FB = FB (sin 30 i + cos 30 j) N
= {0.5 FB i + 0.866 FB j} N
FC = – FC i N
FD = FD (rAD /rAD)
= FD { (1 i – 2 j + 2 k) / (12 + 22 + 22)½ } N
= { 0.333 FD i – 0.667 FD j + 0.667 FD k } N
FBD at A
FC
FD
A
600 N
z
y
30˚
FB
x
1 m
2 m
2 m

## Slide 11: EXAMPLE II (continued)
Solving the three simultaneous equations yields
FC = 646 N (since it is positive, it is as assumed, e.g., in tension)
FD = 900 N
FB = 693 N
y
Now equate the respective i, j, and k components to zero.
 Fx = 0.5 FB – FC + 0.333 FD = 0
 Fy = 0.866 FB – 0.667 FD = 0
 Fz = 0.667 FD – 600 = 0
FBD at A
FC
FD
A
600 N
z
30˚
FB
x
1 m
2 m
2 m

## Slide 12: CONCEPT QUIZ
1. In 3-D, when you know the direction of a force but not its magnitude, how many unknowns corresponding to that force remain?
A) One B) Two C) Three D) Four
2. If a particle has 3-D forces acting on it and is in static equilibrium, the components of the resultant force ( Fx,  Fy, and  Fz ) ___ .
A) have to sum to zero, e.g., -5 i + 3 j + 2 k
B) have to equal zero, e.g., 0 i + 0 j + 0 k
C) have to be positive, e.g., 5 i + 5 j + 5 k
D) have to be negative, e.g., -5 i - 5 j - 5 k
Notes: Answers:
1. A
2. B

## Slide 13: GROUP PROBLEM SOLVING
1) Draw a free body diagram of Point A. Let the unknown force magnitudes be FB, FC, F D .
2) Represent each force in the Cartesian vector form.
3) Apply equilibrium equations to solve for the three unknowns.
Given: A 400 lb crate, as shown, is in equilibrium and supported by two cables and a strut AD.
Find: Magnitude of the tension in each of the cables and the force developed along strut AD.
Plan:
Notes: Source : P3-52

## Slide 14: GROUP PROBLEM SOLVING (continued)
W = weight of crate = - 400 k lb FB = FB(rAB/rAB) = FB {(– 4 i – 12 j + 3 k) / (13)} lb
FC = FC (rAC/rAC) = FC {(2 i – 6 j + 3 k) / (7)}lb
FD = FD( rAD/rAD) = FD {(12 j + 5 k) / (13)}lb
FBD of Point A
x
y
z
W
FB
FC
FD

## Slide 15: GROUP PROBLEM SOLVING (continued)
The particle A is in equilibrium, hence
FB + FC + FD + W = 0
Now equate the respective i, j, k components to zero (i.e., apply the three scalar equations of equilibrium).
 Fx = – (4 / 13) FB + (2 / 7) FC = 0 (1)
 Fy = – (12 / 13) FB – (6 / 7) FC + (12 / 13) FD = 0 (2)
 Fz = (3 / 13) FB + (3 / 7) FC + (5 / 13) FD – 400 = 0 (3)
Solving the three simultaneous equations gives the forces
FB = 274 lb
FC = 295 lb
FD = 547 lb

## Slide 16: ATTENTION QUIZ
2. In 3-D, when you don’t know the direction or the magnitude of a force, how many unknowns do you have corresponding to that force?
A) One B) Two C) Three D) Four
1. Four forces act at point A and point A is in equilibrium. Select the correct force vector P.
A) {-20 i + 10 j – 10 k}lb
B) {-10 i – 20 j – 10 k} lb
C) {+ 20 i – 10 j – 10 k}lb
D) None of the above.
z
F3 = 10 lb
P
F1 = 20 lb
x
A
F2 = 10 lb
y
Notes: Answer
1. D
2. C

## Slide 17
End of the Lecture
Let Learning Continue