## Slide 1: MOMENT OF A FORCE (SCALAR FORMULATION), CROSS PRODUCT, MOMENT OF A FORCE (VECTOR FORMULATION), & PRINCIPLE OF MOMENTS
In-Class Activities :
Reading Quiz
Applications
Moment in 2-D
Moment in 3-D
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objectives :
Students will be able to:
a) understand and define moment, and,
b) determine moments of a force in 2-D and 3-D cases.

## Slide 2: READING QUIZ
1. What is the moment of the 12 N force about point A (MA)?
A) 3 N·m B) 36 N·m C) 12 N·m
D) (12/3) N·m E) 7 N·m
• A
d = 3 m
F = 12 N
2. The moment of force F about point O is defined as MO = ___________ .
A) r × F B) F × r
C) r • F D) r * F
Notes: Answers:
1. B
2. A

## Slide 3: APPLICATIONS
Beams are often used to bridge gaps in walls. We have to know what the effect of the force on the beam will have on the supports of the beam.
What do you think is happening at points A and B?

## Slide 4: APPLICATIONS (continued)
Carpenters often use a hammer in this way to pull a stubborn nail. Through what sort of action does the force FH at the handle pull the nail? How can you mathematically model the effect of force FH at point O?

## Slide 5: MOMENT OF A FORCE - SCALAR FORMULATION (Section 4.1)
The moment of a force about a point provides a measure of the tendency for rotation (sometimes called a torque).

## Slide 6: MOMENT OF A FORCE - SCALAR FORMULATION (continued)
As shown, d is the perpendicular distance from point O to the line of action of the force.
In 2-D, the direction of MO is either clockwise (CW) or counter-clockwise (CCW), depending on the tendency for rotation.
In a 2-D case, the magnitude of the moment is Mo = F d

## Slide 7: MOMENT OF A FORCE - SCALAR FORMULATION (continued)
Often it is easier to determine MO by using the components of F as shown.
Then MO = (Fy a) – (Fx b). Note the different signs on the terms! The typical sign convention for a moment in 2-D is that counter-clockwise is considered positive. We can determine the direction of rotation by imagining the body pinned at O and deciding which way the body would rotate because of the force.
For example, MO = F d and the direction is counter-clockwise.
F
a
b
d
O
a
b
O
F
F x
F y

## Slide 8: VECTOR CROSS PRODUCT (Section 4.2)
While finding the moment of a force in 2-D is straightforward when you know the perpendicular distance d, finding the perpendicular distances can be hard—especially when you are working with forces in three dimensions.
So a more general approach to finding the moment of a force exists. This more general approach is usually used when dealing with three dimensional forces but can be used in the two dimensional case as well.
This more general method of finding the moment of a force uses a vector operation called the cross product of two vectors.

## Slide 9: CROSS PRODUCT (Section 4.2)
In general, the cross product of two vectors A and B results in another vector, C , i.e., C = A  B. The magnitude and direction of the resulting vector can be written as
C = A  B = A B sin  uC
As shown, uC is the unit vector perpendicular to both A and B vectors (or to the plane containing the A and B vectors).

## Slide 10: CROSS PRODUCT (continued)
The right-hand rule is a useful tool for determining the direction of the vector resulting from a cross product.
For example: i  j = k
Note that a vector crossed into itself is zero, e.g., i  i = 0

## Slide 11: CROSS PRODUCT (continued)
Also, the cross product can be written as a determinant.
Each component can be determined using 2  2 determinants.

## Slide 12: MOMENT OF A FORCE – VECTOR FORMULATION (Section 4.3)
Using the vector cross product, MO = r  F.
Here r is the position vector from point O to any point on the line of action of F.
Moments in 3-D can be calculated using scalar (2-D) approach, but it can be difficult and time consuming. Thus, it is often easier to use a mathematical approach called the vector cross product.

## Slide 13: MOMENT OF A FORCE – VECTOR FORMULATION (continued)
By expanding the above equation using 2  2 determinants (see Section 4.2), we get (sample units are N - m or lb - ft)
MO = (ry Fz - rz Fy) i  (rx Fz - rz Fx ) j + (rx Fy - ry Fx ) k
The physical meaning of the above equation becomes evident by considering the force components separately and using a 2-D formulation.
So, using the cross product, a moment can be expressed as

## Slide 14: EXAMPLE I
1) Resolve the 100 N force along x and y-axes.
2) Determine MO using a scalar analysis for the two force components and then add those two moments together.
Given: A 100 N force is applied to the frame.
Find: The moment of the force at point O.
Plan:
Notes: Source : F4-1

## Slide 15: EXAMPLE I (continued)
Solution:
+  Fy = – 100 (3/5) N
+  Fx = 100 (4/5) N
+ MO = {– 100 (3/5)N (5 m) – (100)(4/5)N (2 m)} N·m
= – 460 N·m or 460 N·m CW

## Slide 16: EXAMPLE II
1) Find F = F1 + F2 and rOA.
2) Determine MO = rOA  F .
o
Given: F1={100 i - 120 j + 75 k}lb
F2={-200 i +250 j + 100 k}lb
Find: Resultant moment by the forces about point O.
Plan:
Notes: Source : F4-12

## Slide 17: EXAMPLE II (continued)
Solution:
First, find the resultant force vector F
F = F1 + F2
= { (100 - 200) i + (-120 + 250) j + (75 + 100) k} lb
= {-100 i +130 j + 175 k} lb
Find the position vector rOA
rOA = {4 i + 5 j + 3 k} ft
i
j
k
4 5 3
-100 130 175
MO =
= [{5(175) – 3(130)} i – {4(175) – 3(-100)} j + {4(130) – 5(-100)} k] ft·lb
= {485 i – 1000 j + 1020 k} ft·lb
Then find the moment by using the vector cross product.

## Slide 18: CONCEPT QUIZ
P
Q
R
S
1. If a force of magnitude F can be applied in four different 2-D configurations (P,Q,R, & S), select the cases resulting in the maximum and minimum torque values on the nut. (Max, Min).
A) (Q, P) B) (R, S)
C) (P, R) D) (Q, S)
2. If M = r  F, then what will be the value of M • r?
A) 0 B) 1
  C) r 2 F D) None of the above.
Notes: Answers:
1. D
2. A

## Slide 19: GROUP PROBLEM SOLVING I
Since this is a 2-D problem:
1) Resolve the 20 lb force along the handle’s x and y axes.
2) Determine MA using a scalar analysis.
Given: A 20 lb force is applied to the hammer.
Find: The moment of the force at A.
Plan:
x
y
Notes: Source : P4-20

## Slide 20: GROUP PROBLEM SOLVING I (continued)
Solution:
+  Fy = 20 sin 30° lb
+  Fx = 20 cos 30° lb
+ MA = {–(20 cos 30°)lb (18 in) – (20 sin 30°)lb (5 in)}
= – 361.77 lb·in = 362 lb·in (clockwise or CW)
x
y

## Slide 21: GROUP PROBLEM SOLVING II
1) Find F and rAC.
2) Determine MA = rAC  F
Given: The force and geometry shown.
Find: Moment of F about point A
Plan:
Notes: Source : P4-43

## Slide 22: GROUP PROBLEM SOLVING II (continued)
Solution:
F ={ (80 cos30) sin 40 i
+ (80 cos30) cos 40 j  80 sin30 k} N
={44.53 i + 53.07 j  40 k } N
rAC ={0.55 i + 0.4 j  0.2 k } m
MA =
= { -5.39 i + 13.1 j +11.4 k } N·m
i j k
0.55 0.4  0.2
44.53 53.07  40
Find the moment by using the cross product.

## Slide 23: ATTENTION QUIZ
2. If r = { 5 j } m and F = { 10 k } N, the moment
r × F equals { _______ } N·m.
A) 50 i B) 50 j C) –50 i
D) – 50 j E) 0
10 N
3 m P 2 m
5 N
1. Using the CCW direction as positive, the net moment of the two forces about point P is
A) 10 N  m B) 20 N  m C) - 20 N  m
D) 40 N  m E) - 40 N  m
Notes: Answers:
1. B
2. A

## Slide 24
End of the Lecture
Let Learning Continue