## Slide 1: MOMENT ABOUT AN AXIS
In-Class Activities:
Check Homework
Reading Quiz
Applications
Scalar Analysis
Vector Analysis
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objectives:
Students will be able to determine the moment of a force about an axis using
a) scalar analysis, and,
b) vector analysis.

## Slide 2: READING QUIZ
1. When determining the moment of a force about a specified axis, the axis must be along _____________.
A) the x axis B) the y axis C) the z axis
D) any line in 3-D space E) any line in the x-y plane
2. The triple scalar product u • ( r  F ) results in
A) a scalar quantity ( + or - ). B) a vector quantity.
C) zero. D) a unit vector.
E) an imaginary number.
Notes: 1. D
2. A

## Slide 3: APPLICATIONS
With the force P, a person is creating a moment MA using this flex-handle socket wrench. Does all of MA act to turn the socket? How would you calculate an answer to this question?

## Slide 4: APPLICATIONS (continued)
Sleeve A of this bracket can provide a maximum resisting moment of 125 N·m about the x-axis. How would you determine the maximum magnitude of F before turning about the x-axis occurs?

## Slide 5: SCALAR ANALYSIS
Recall that the moment of a scalar force about any point O is MO= F dO where dO is the perpendicular (or shortest) distance from the point to the force’s line of action. This concept can be extended to find the moment of a force about an axis.
Finding the moment of a force about an axis can help answer the types of questions we just considered.

## Slide 6: SCALAR ANALYSIS (continued)
In the figure above, the moment about the y-axis would be My= Fz (dx) = F (r cos θ). However, unless the force can easily be broken into components and the “dx” found quickly, such calculations are not always trivial and vector analysis may be much easier (and less likely to produce errors).

## Slide 7: VECTOR ANALYSIS
First compute the moment of F about any arbitrary point O that lies on the a-axis using the cross product.
MO = r  F
Now, find the component of MO along the a-axis using the dot product.
Ma = ua • MO
Our goal is to find the moment of F (the tendency to rotate the body) about the a-axis.

## Slide 8: VECTOR ANALYSIS (continued)
In the this equation,
ua represents the unit vector along the a-axis,
r is the position vector from any point on the a-axis to any point A on the line of action of the force, and
F is the force vector.
Ma can also be obtained as
The above equation is also called the triple scalar product.

## Slide 9: EXAMPLE
Use Mz = u • (r  F ).
First, find F in Cartesian vector form.
Note that u = 1 i in this case.
4) The vector r is the position vector from O to A.
A
B
Given: A force is applied to the tool as shown.
Find: The magnitude of the moment of this force about the x axis of the value.
Plan:
Notes: Source : F4-15

## Slide 10: EXAMPLE (continued)
Solution:
u = 1 i
rOA = {0 i + 0.3 j + 0.25 k} m
F = 200 (cos 120 i + cos 60 j + cos 45 k) N
= {-100 i + 100 j + 141.4 k} N
Now find Mz = u • (rOA  F )
1 0 0
0 0.3 0.25
-100 100 141.4
Mz =
= 1{0.3 (141.4) – 0.25 (100) } N·m
Mz = 17.4 N·m CCW

## Slide 11: CONCEPT QUIZ
1. The vector operation (P  Q) • R equals
A) P  (Q • R).
B) R • (P  Q).
C) (P • R)  (Q • R).
D) (P  R) • (Q  R ).
Notes: Answers:
1.B

## Slide 12: CONCEPT QUIZ (continued)
2. The force F is acting along DC. Using the triple scalar product to determine the moment of F about the bar BA, you could use any of the following position vectors except ______.
A) rBC B) rAD
C) rAC D) rDB
E) rBD
Notes: ANSWER:
2. D

## Slide 13: GROUP PROBLEM SOLVING
1) Find ua and rOA
2) Find F in Cartesian vector form.
3) Use Ma = ua • (rOA  F)
Given: The force of F = 30 N acts on the bracket.  = 60,  = 60,  = 45.
Find: The moment of F about the a-a axis.
Plan:


rOA
A
O
ua
Notes: Source : P4-66

## Slide 14: GROUP PROBLEM SOLVING (continued)
ua = j
rOA = {– 0.1 i + 0.15 k} m
Solution:
F = 30 {cos 60 i + cos 60 j + cos 45 k} N
F = { 15 i + 15 j + 21.21 k} N


rOA
A
O
ua

## Slide 15: GROUP PROBLEM SOLVING (continued)
Ma = -1 {-0.1 (21.21) – 0.15 (15)}
= 4.37 N·m
Now find the triple product, Ma = ua • (rOA  F)
Ma =
0 1 0
- 0.1 0 0.15
15 15 21.21
N·m


rOA
A
O
ua
Ma

## Slide 16: ATTENTION QUIZ
1. For finding the moment of the force F about the x-axis, the position vector in the triple scalar product should be ___ .
A) rAC B) rBA
C) rAB D) rBC
2. If r = {1 i + 2 j} m and F = {10 i + 20 j + 30 k} N, then the moment of F about the y-axis is ____ N·m.
A) 10 B) -30
C) -40 D) None of the above.
Notes: ANSWERS:
1. C
2. B

## Slide 17
End of the Lecture
Let Learning Continue