## Slide 1: MOMENT OF A COUPLE
In-Class activities:
Check Homework
Reading Quiz
Applications
Moment of a Couple
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objectives:
Students will be able to
a) define a couple, and,
b) determine the moment of a couple.

## Slide 2: READING QUIZ
1. In statics, a couple is defined as __________ separated by a perpendicular distance.
A) two forces in the same direction
B) two forces of equal magnitude
C) two forces of equal magnitude acting in the same direction
D) two forces of equal magnitude acting in opposite directions
2. The moment of a couple is called a _________ vector.
A) Free B) Spinning
C) Fixed D) Sliding
Notes: Answers:
1. D
2. A

## Slide 3: APPLICATIONS
A torque or moment of 12 N·m is required to rotate the wheel. Why does one of the two grips of the wheel above require less force to rotate the wheel?

## Slide 4: APPLICATIONS (continued)
Would older vehicles without power steering have needed larger or smaller steering wheels?
When you grip a vehicle’s steering wheel with both hands and turn, a couple moment is applied to the wheel.

## Slide 5: MOMENT OF A COUPLE
The moment of a couple is defined as
MO = F d (using a scalar analysis) or as
MO = r  F (using a vector analysis).
Here r is any position vector from the line of action of F to the line of action of F.
A couple is defined as two parallel forces with the same magnitude but opposite in direction separated by a perpendicular distance “d.”

## Slide 6: MOMENT OF A COUPLE (continued)
Moments due to couples can be added together using the same rules as adding any vectors.
The net external effect of a couple is that the net force equals zero and the magnitude of the net moment equals F *d.
Since the moment of a couple depends only on the distance between the forces, the moment of a couple is a free vector. It can be moved anywhere on the body and have the same external effect on the body.

## Slide 7: EXAMPLE I : SCALAR APPROACH
1) Add the two couples to find the resultant couple.
2) Equate the net moment to 1.5 kNm clockwise to find F.
Given: Two couples act on the beam with the geometry shown.
Find: The magnitude of F so that the resultant couple moment is 1.5 kNm clockwise.
Plan:
Notes: Source : F4-21

## Slide 8: EXAMPLE I : SCALAR APPROACH (continued)
Solution:
The net moment is equal to:
+  M = – F (0.9) + (2) (0.3)
= – 0.9 F + 0.6
– 1.5 kNm = – 0.9 F + 0.6
Solving for the unknown force F, we get
F = 2.33 kN

## Slide 9: EXAMPLE II : VECTOR APPROACH
1) Use M = r  F to find the couple moment.
2) Set r = rAB and F = FB.
3) Calculate the cross product to find M.
Given: A 450 N force couple acting on the pipe assembly.
Find: The couple moment in Cartesian vector notation.
Plan:
rAB
FB
Notes: Source : F4-24

## Slide 10: EXAMPLE II: VECTOR APPROACH (continued)
= [{0(-270) – 0(360)} i – {4(-270) – 0(0)} j + {0.4(360) – 0(0)} k] N·m
= {0 i + 108 j + 144 k} N·m
M = rAB  FB
=
N·m
i j k
0.4 0 0
0 360 270
rAB = { 0.4 i } m
FB = {0 i + 450(4/5) j  450(3/5) k} N
= {0 i + 360 j  270 k} N
rAB
FB
Solution:

## Slide 11: CONCEPT QUIZ
2. If three couples act on a body, the overall result is that
A) The net force is not equal to 0.
B) The net force and net moment are equal to 0.
C) The net moment equals 0 but the net force is not necessarily equal to 0.
D) The net force equals 0 but the net moment is not necessarily equal to 0 .
1. F1 and F2 form a couple. The moment of the couple is given by ____ .
A) r1  F1 B) r2  F1
C) F2  r1 D) r2  F2
F1
F2
r1
r2
Notes: Answers:
1. B
2. D

## Slide 12: GROUP PROBLEM SOLVING I
1) Resolve the forces in x and y-directions so they can be treated as couples.
2) Add these two couples to find the resultant couple.
Given: Two couples act on the beam with the geometry shown and d = 4 ft.
Find: The resultant couple
Plan:
Notes: Source : P4-80

## Slide 13: GROUP PROBLEM SOLVING I (continued)
No! Only the 43.30 lb components create a couple. Why?
The x and y components of the upper-left 50 lb force are:
50 lb (cos 30) = 43.30 lb vertically up
50 lb (sin 30) = 25 lb to the right
Do both of these components form couples with their matching components of the other 50 force?

## Slide 14: GROUP PROBLEM SOLVING I (continued)
The net moment is equal to:
+ M = – (43.3 lb)(3 ft) + (64 lb)(4 ft)
= – 129.9 + 256 = 126 ft·lb CCW
Now resolve the lower 80 lb force:
(80 lb) (3/5), acting up
(80 lb) (4/5), acting to the right
Do both of these components create a couple with components of the other 80 lb force?
d = 4 ft

## Slide 15: GROUP PROBLEM SOLVING II
1) Use M = r  F to find the couple moment.
2) Set r = rAB and F = {80 k} N.
3) Calculate the cross product to find M.
Given: F = {80 k} N and
– F = {– 80 k} N
Find: The couple moment acting on the pipe assembly using Cartesian vector notation.
Plan:
rAB
Notes: Source : P4-92

## Slide 16: GROUP PROBLEM SOLVING II (continued)
= {(40 – 0) i – (8 – 0) j + (0) k} N · m
= { 40 i – 8 j } N · m
rAB = { (0.3 – 0.2 ) i + (0.8 – 0.3) j + (0 – 0) k } m
= { 0.1 i + 0.5 j } m
F = {80 k} N
i
=
M = rAB  F
N · m
j
k
0.1 0.5 0
0 0 80

## Slide 17: ATTENTION QUIZ
1. A couple is applied to the beam as shown. Its moment equals _____ N·m.
A) 50 B) 60
C) 80 D) 100
3
4
5
1m
2m
50 N
2. You can determine the couple moment as M = r  F
If F = { -20 k} lb, then r is
A) rBC B) rAB
C) rCB D) rBA
Notes: Answers:
1. B
2. D

## Slide 18
End of the Lecture
Let Learning Continue