## Slide 1: SIMPLIFICATION OF FORCE AND COUPLE SYSTEMS & THEIR FURTHER SIMPLIFICATION
Today’s Objectives:
Students will be able to:
Determine the effect of moving a force.
b) Find an equivalent force-couple system for a system of forces and couples.
In-Class Activities:
Check Homework
Reading Quiz
Applications
Equivalent Systems
System Reduction
Concept Quiz
Group Problem Solving
Attention Quiz

## Slide 2: READING QUIZ
1. A general system of forces and couple moments acting on a rigid body can be reduced to a ___ .
A) single force
B) single moment
C) single force and two moments
D) single force and a single moment
2. The original force and couple system and an equivalent force-couple system have the same _____ effect on a body.
A) internal B) external
C) internal and external D) microscopic
Notes: Answers:
1. D
2. B

## Slide 3: APPLICATIONS
What are the resultant effects on the person’s hand when the force is applied in these four different ways?
Why is understanding these differences important when designing various load-bearing structures?

## Slide 4: APPLICATIONS (continued)
Several forces and a couple moment are acting on this vertical section of an I-beam.
For the process of designing the I-beam, it would be very helpful if you could replace the various forces and moment just one force and one couple moment at point O with the same external effect? How will you do that?
| |
??

## Slide 5: SIMPLIFICATION OF FORCE AND COUPLE SYSTEM (Section 4.7)
When a number of forces and couple moments are acting on a body, it is easier to understand their overall effect on the body if they are combined into a single force and couple moment having the same external effect.
The two force and couple systems are called equivalent systems since they have the same external effect on the body.

## Slide 6: MOVING A FORCE ON ITS LINE OF ACTION
Moving a force from A to B, when both points are on the vector’s line of action, does not change the external effect.
Hence, a force vector is called a sliding vector. (But the internal effect of the force on the body does depend on where the force is applied).

## Slide 7: MOVING A FORCE OFF OF ITS LINE OF ACTION
When a force is moved, but not along its line of action, there is a change in its external effect!
Essentially, moving a force from point A to B (as shown above) requires creating an additional couple moment. So moving a force means you have to “add” a new couple.
Since this new couple moment is a “free” vector, it can be applied at any point on the body.
B

## Slide 8: SIMPLIFICATION OF A FORCE AND COUPLE SYSTEM
When several forces and couple moments act on a body, you can move each force and its associated couple moment to a common point O.
Now you can add all the forces and couple moments together and find one resultant force-couple moment pair.

## Slide 9: SIMPLIFICATION OF A FORCE AND COUPLE SYSTEM (continued)
If the force system lies in the x-y plane (a 2-D case), then the reduced equivalent system can be obtained using the following three scalar equations.
WR = W1 + W2
(MR)o = W1 d1 + W2 d2

## Slide 10: FURTHER SIMPLIFICATION OF A FORCE AND COUPLE SYSTEM (Section 4.8)
=
=
In three special cases, concurrent, coplanar, and parallel systems of forces, the system can always be reduced to a single force.
If FR and MRO are perpendicular to each other, then the system can be further reduced to a single force, FR , by simply moving FR from O to P.

## Slide 11: EXAMPLE I
1) Sum all the x and y components of the forces to find FRA.
2) Find and sum all the moments resulting from moving each force component to A.
3) Shift FRA to a distance d such that d = MRA/FRy
Given: A 2-D force system with geometry as shown.
Find: The equivalent resultant force and couple moment acting at A and then the equivalent single force location measured from A.
Plan:
Notes: Source : F4-32

## Slide 12: EXAMPLE I (continued)
FR = ( 852 + 163.32 )1/2 = 184 lb
 = tan-1 ( 163.3/85) = 62.5°
The equivalent single force FR can be located at a distance d measured from A.
d = MRA/FRy = 509.7 / 163.3 = 3.12 ft
FR
+ FRx= 50(sin 30) + 100(3/5)
= 85 lb
+  FRy= 200 + 50(cos 30) – 100(4/5)
= 163.3 lb
+ MRA = 200 (3) + 50 (cos 30) (9)
– 100 (4/5) 6 = 509.7 lb·ft CCW

## Slide 13: EXAMPLE II
1) Find FRO = Fi = FRzo k
2) Find MRO =  (ri  Fi) = MRxO i + MRyO j
3) The location of the single equivalent resultant force is given as x = – MRyO / FRzO and y = MRxO / FRzO
Given: The slab is subjected to three parallel forces.
Find: The equivalent resultant force and couple moment at the origin O. Also find the location (x, y) of the single equivalent resultant force.
Plan:
Notes: Source : F4-35

## Slide 14: EXAMPLE II (continued)
FRO = {100 k – 500 k – 400 k} = – 800 k N
MRO = (3 i)  (100 k) + (4 i + 4 j)  (-500 k)
+ (4 j)  (-400 k)
= {–300 j + 2000 j – 2000 i – 1600 i}
= { – 3600 i + 1700 j }N·m
The location of the single equivalent resultant force is given as,
x = – MRyo / FRzo = (–1700) / (–800) = 2.13 m
y = MRxo / FRzo = (–3600) / (–800) = 4.5 m

## Slide 15: CONCEPT QUIZ
2. Consider two couples acting on a body. The simplest possible equivalent system at any arbitrary point on the body will have
A) One force and one couple moment.
B) One force.
C) One couple moment.
D) Two couple moments.
1. The forces on the pole can be reduced to a single force and a single moment at point ____ .
A) P B) Q C) R
D) S E) Any of these points.




y
z
P
Q
R
S
x
Notes: Answers:
1. E
2. C

## Slide 16: GROUP PROBLEM SOLVING I
1) Sum all the x and y components of the two forces to find FRA.
2) Find and sum all the moments resulting from moving each force to A and add them to the 1500 Nm free moment to find the resultant MRA .
Given: A 2-D force and couple system as shown.
Find: The equivalent resultant force and couple moment acting at A.
Plan:
Notes: Source : P4-117

## Slide 17: GROUP PROBLEM SOLVING I (continued)
+ Fx = 450 (cos 60) – 700 (sin 30)
= – 125 N
+  Fy = – 450 (sin 60) – 300 – 700 (cos 30)
= – 1296 N
Summing the force components:
+ MRA = 450 (sin 60) (2) + 300 (6) + 700 (cos 30) (9) + 1500
= 9535 Nm
Now find the magnitude and direction of the resultant.
FRA = (1252 + 12962)1/2 = 1302 N and  = tan-1 (1296 /125) = 84.5°

## Slide 18: GROUP PROBLEM SOLVING II
Given: Forces and couple moments are applied to the pipe.
Find: An equivalent resultant force and couple moment at point O.
Plan:
a) Find FRO =  Fi = F1 + F2+ F3
b) Find MRO =  MC +  ( ri  Fi )
where,
MC are any free couple moments.
ri are the position vectors from the point O to any point on the line of action of Fi .
Notes: Source : P4-134

## Slide 19: GROUP PROBLEM SOLVING II (continued)
F1 = {300 k} N
F2 = 200{cos45 i – sin 45 k} N
= {141.4 i – 141.4 k} N
F3 = {100 j} N
r1 = {0.5 i } m, r2 = {1.1 i } m,
r3 = {1.9 i } m
MC1 = {100 k} Nm
MC2 = 180{cos45 i – sin 45k}Nm
= {127.3 i – 127.3k}Nm
Free couple moments are:
F1
F2
F3
MC1
MC2

## Slide 20: GROUP PROBLEM SOLVING II (continued)
MRO =  MC +  ( ri  Fi )
+
i j k
0 0.5 0
0 0 300
i j k
0 1.1 0
141.4 0 -141.4
+
MRO = {100 k} + {127.3 i – 127.3k}
i j k
0 1.9 0
0 100 0
+
MRO = {122 i – 183 k} Nm
Resultant force and couple moment at point O:
FRO =  Fi = F1 + F2+ F3
= {300 k}+{141.4 i – 141.4 k} + {100 j}
FRO = {141 i + 100 j + 159 k} N
F1
F2
F3
MC1
MC2

## Slide 21: ATTENTION QUIZ
1. For this force system, the equivalent system at P is ___________ .
A) FRP = 40 lb (along +x-dir.) and MRP = +60 ft ·lb
B) FRP = 0 lb and MRP = +30 ft · lb
C) FRP = 30 lb (along +y-dir.) and MRP = -30 ft ·lb
D) FRP = 40 lb (along +x-dir.) and MRP = +30 ft ·lb
P
1'
1'
30 lb
40 lb
30 lb
•
x
y
Notes: Answer:
1. D

## Slide 22: ATTENTION QUIZ
2. Consider three couples acting on a body. Equivalent systems will be _______ at different points on the body.
A) Different when located
B) The same even when located
C) Zero when located
D) None of the above.
Notes: Answer:
2. B

## Slide 23
End of the Lecture
Let Learning Continue