## Slide 1: 3-D FREE-BODY DIAGRAMS, EQUILIBRIUM EQUATIONS, CONSTRAINTS AND STATICAL DETERMINACY
In-Class Activities:
Check Homework, if any
Reading Quiz
Applications
Support Reactions in 3-D
Equations of Equilibrium
Concept Quiz
Group Problem Solving
Attention quiz
Today’s Objective:
Students will be able to:
a) Identify support reactions in 3-D and draw a free-body diagram, and,
b) Apply the equations of equilibrium.

## Slide 2: READING QUIZ
1. If a support prevents rotation of a body about an axis, then the support exerts a ________ on the body about that axis.
  A) Couple moment B) Force
  C) Both A and B. D) None of the above.
When doing a 3-D problem analysis, you have ________ scalar equations of equilibrium.
A) 3 B) 4
  C) 5 D) 6
Notes: ANSWERS:
1. A
2. D

## Slide 3: APPLICATIONS
Ball-and-socket joints and journal bearings are often used in mechanical systems. To design the joints or bearings, the support reactions at these joints and the loads must be determined.

## Slide 4: APPLICATIONS (continued)
If A is moved to a lower position D, will the force in the rod change or remain the same? By making such a change without understanding if there is a change in forces, failure might occur.
The tie rod from point A is used to support the overhang at the entrance of a building. It is pin connected to the wall at A and to the center of the overhang B.

## Slide 5: APPLICATIONS (continued)
The floor crane, which weighs 350 lb, is supporting a oil drum.
How do you determine the largest oil drum weight that the crane can support without overturning?

## Slide 6: SUPPORT REACTIONS IN 3-D (Table 5-2)
As a general rule, if a support prevents translation of a body in a given direction, then a reaction force acting in the opposite direction is developed on the body. Similarly, if rotation is prevented, a couple moment is exerted on the body by the support.
A few examples of supports are shown above. Other support reactions are given in your textbook (Table 5-2).

## Slide 7: IMPORTANT NOTE
A single bearing or hinge can prevent rotation by providing a resistive couple moment. However, it is usually preferred to use two or more properly aligned bearings or hinges. In these cases, only force reactions are generated and no moment reactions are created.

## Slide 8: EQUATIONS OF EQUILIBRIUM (Section 5.6)
As stated earlier, when a body is in equilibrium, the net force and the net moment equal zero, i.e.,  F = 0 and  MO = 0 .
These two vector equations can be written as six scalar equations of equilibrium (E-of-E). These are
FX =  FY =  FZ = 0
MX =  MY =  MZ = 0
The moment equations can be determined about any point. Usually, choosing the point where the maximum number of unknown forces are present simplifies the solution. Any forces passing through the point where moments are taken do not appear in the moment equation.

## Slide 9: CONSTRAINTS AND STATICAL DETERMINACY (Section 5.7)
Redundant Constraints: When a body has more supports than necessary to hold it in equilibrium, it becomes statically indeterminate.
A problem that is statically indeterminate has more unknowns than equations of equilibrium.
Are statically indeterminate structures used in practice? Why or why not?

## Slide 10: IMPROPER CONSTRAINTS
In some cases, there may be as many unknown reactions as there are equations of equilibrium.
However, if the supports are not properly constrained, the body may become unstable for some loading cases.
Here, while we have 6 unknowns, there is nothing restricting rotation about the AB axis!

## Slide 11: EXAMPLE I
a) Use the established x, y and z-axes.
b) Draw a FBD of the rod.
c) Write the forces using scalar equations.
d) Apply scalar equations of equilibrium to solve for the unknown forces.
Given: The rod, supported by thrust bearing at A and cable BC, is subjected to an 80 lb force.
Find: Reactions at the thrust bearing A and cable BC.
Plan:
Notes: Source : F5-12

## Slide 12: EXAMPLE I (continued)
Applying scalar equations of equilibrium in appropriate order, we get
F X = AX = 0; AX = 0
F Z = AZ + FBC – 80 = 0;
M Y = – 80 ( 1.5 ) + FBC ( 3.0 ) = 0;
Solving the last two equations: FBC = 40 lb, AZ = 40 lb
FBD of the rod:

## Slide 13: EXAMPLE I (continued)
FBD of the rod
M X = ( MA) X + 40 (6) – 80 (6) = 0 ; (MA ) X= 240 lb ft CCW
M Z = ( MA) Z = 0 ; (MA ) Z = 0
= 40 lb
Now write scalar moment equations about what point?
Point A!

## Slide 14: EXAMPLE II
a) Use established x, y and z-axes.
b) Draw a FBD of the plate.
c) Write the forces using scalar equations.
d) Apply scalar equations of equilibrium to solve for the unknown forces.
Given: The uniform plate has a weight of 500 lb, supported by three cables.
Find: The tension in each of the supporting cables.
Plan:
Notes: Source : F5-7

## Slide 15: EXAMPLE II (continued)
FBD of the plate:
Applying scalar equations of equilibrium:
 Fz = TA + TB + TC – 200 – 500 = 0 (1)
 Mx = TA (3) + TC (3) – 500 (1.5) – 200 (3) = 0 (2)
 My = – TB (4) – TC (4) + 500 (2) + 200 (2) = 0 (3)
1.5 ft
TB
TA
TC
500 lb
200 lb

## Slide 16: EXAMPLE II (continued)
 Fz = TA + TB + TC – 200 – 500 = 0 (1)
 Mx = TA (3) + TC (3) – 500 (1.5) – 200 (3) = 0 (2)
 My = – TB (4) – TC (4) + 500 (2) + 200 (2) = 0 (3)
Using Eqs. (2) and (3), express TA and TB in terms of TC:
Eq. (2)  TA = 450 – TC
Eq. (3)  TB = 350 – TC
Substituting the results into Eq. (1) & solving for TC
Eq. (1)  (450 – TC ) + (350 – TC) + TC – 200 – 500 = 0
TC = 100 lb 
TA = 350 lb  and TB = 250 lb 

## Slide 17: CONCEPT QUIZ
1. The rod AB is supported using two cables at B and a ball-and-socket joint at A. How many unknown support reactions exist in this problem?
A) Five force and one moment reaction
B) Five force reactions
C) Three force and three moment reactions
D) Four force and two moment reactions
Notes: ANSWERS :
1. B

## Slide 18: CONCEPT QUIZ (continued)
2. If an additional couple moment in the vertical direction is applied to rod AB at point C, then what will happen to the rod?
A) The rod remains in equilibrium as the cables provide the necessary support reactions.
B) The rod remains in equilibrium as the ball-and-socket joint will provide the necessary resistive reactions.
C) The rod becomes unstable as the cables cannot support compressive forces.
D) The rod becomes unstable since a moment about AB cannot be restricted.
Notes: ANSWERS:
2. D

## Slide 19: GROUP PROBLEM SOLVING
a) Draw a FBD of the rod.
b) Apply scalar equations of equilibrium to solve for the unknowns.
Given: A bent rod is supported by smooth journal bearings at A, B, and C. F=800 N. Assume the rod is properly aligned.
Find: The reactions at all the supports.
Plan:
Notes: Source : P5-73

## Slide 20: GROUP PROBLEM SOLVING (continued)
The x, y and z components of force F are
Fx = (800 cos 60°) cos 30° = 346.4 N
Fy = (800 cos 60°) sin 30° = 200 N
Fz = 800 sin 60° = 692.8 N
F = 346.4 i + 200 j + 692.8 k
A FBD of the rod
F
Cx
Cy
By
Bz
Ax
Az
y
x
z
2 m
0.75 m
1 m
2 m

## Slide 21: GROUP PROBLEM SOLVING (continued)
Applying scalar equations of equilibrium, we get
 Fx = Ax + Cx + 346.4 = 0 (1)
 Fy = 200 + By + Cy = 0 (2)
 Fz = Az + Bz – 692.8 = 0 (3)
 Mx = – Cy (2) + Bz (2) – 692.8(2) = 0 (4)
 My = Bz (1) + Cx (2) = 0 (5)
 Mz = – Cy (1.75) – Cx (2) – By (1) – 346.4(2) = 0 (6)
Solving Eqs. (1) to (6),
Ax = -400 N, By = 600 N, Cx = 53.6 N
Az = 800 N, Bz = -107 N, Cy = -800 N
A FBD of the rod
F
Cx
Cy
By
Bz
Ax
Az
y
x
z
2 m
0.75 m
1 m
2 m
Recall F = 346.4 i + 200 j + 692.8 k

## Slide 22: ATTENTION QUIZ
1. A plate is supported by a ball-and-socket joint at A, a roller joint at B, and a cable at C. How many unknown support reactions are there in this problem?
A) Four forces and two moments
B) Six forces
C) Five forces
D) Four forces and one moment
Notes: ANSWER:
1. C

## Slide 23: ATTENTION QUIZ
2. What will be the easiest way to determine the force reaction BZ ?
A) Scalar equation  FZ = 0
B) Vector equation  MA = 0
C) Scalar equation  MZ = 0
D) Scalar equation  MY = 0
Notes: ANSWERS:
2. D

## Slide 24
End of the Lecture
Let Learning Continue