## Slide 1: FRAMES AND MACHINES
In-Class Activities:
Check Homework, if any
Reading Quiz
Applications
Analysis of a Frame/Machine
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objectives:
Students will be able to:
a) Draw the free body diagram of a frame or machine and its members.
b) Determine the forces acting at the joints and supports of a frame or machine.

## Slide 2: READING QUIZ
1. Frames and machines are different as compared to trusses since they have ___________.
  A) Only two-force members B) Only multiforce members
  C) At least one multiforce member D) At least one two-force member
2. Forces common to any two contacting members act with _______ on the other member.
  A) Equal magnitudes but opposite sense
  B) Equal magnitudes and the same sense
  C) Different magnitudes and the opposite sense
  D) Different magnitudes and the same sense
Notes: Answers:
1. C
2. A

## Slide 3: APPLICATIONS
How is a frame different than a truss?
To be able to design a frame, you need to determine the forces at the joints and supports.
Frames are commonly used to support various external loads.

## Slide 4: APPLICATIONS (continued)
How can you determine the loads at the joints and supports? These forces and moments are required when designing the machine’s members.
“Machines,” like those above, are used in a variety of applications. How are they different from trusses and frames?

## Slide 5: FRAMES AND MACHINES: DEFINITIONS
Frames are generally stationary and support external loads.
Machines contain moving parts and are designed to alter the effect of forces.
Frames and machines are two common types of structures that have at least one multi-force member. (Recall that trusses have nothing but two-force members).
Frame
Machine

## Slide 6: STEPS FOR ANALYZING A FRAME OR MACHINE
1. Draw a FBD of the frame or machine and its members, as necessary.
Hints: a) Identify any two-force members,
b) Note that forces on contacting surfaces (usually between a pin and a member) are equal and opposite, and,
c) For a joint with more than two members or an external force, it is advisable to draw a FBD of the pin.
FAB

## Slide 7: STEPS FOR ANALYZING A FRAME OR MACHINE
2. Develop a strategy to apply the equations of equilibrium to solve for the unknowns. Look for ways to form single equations and single unknowns.
Problems are going to be challenging since there are usually several unknowns. A lot of practice is needed to develop good strategies and ease of solving these problems.
FAB

## Slide 8: EXAMPLE
a) Draw a FBD of frame member BC. Why pick this part of the frame?
b) Apply the equations of equilibrium and solve for the unknowns at C and B.
Given: The frame supports an external load and moment as shown.
Find: The horizontal and vertical components of the pin reactions at C and the magnitude of reaction at B.
Plan:
Notes: Source : F6-16

## Slide 9: EXAMPLE (continued)
Note that member AB is a two-force member.
Equations of Equilibrium:
Start with  MC since it yields one unknown.
+  MC = – FAB (3/ (1) – FAB (1/ (3) + 800 + 400 (2) = 0
FAB = 843.3 = 843 N
FBD of member BC
CX
CY
B
FAB
400 N
1 m
2 m
1 m
800 N m
1
3

## Slide 10: EXAMPLE (continued)
 +  FY = – CY + 843.3 (1/ – 400 = 0
CY = – 133 N = 133 N 
+  FX = – CX – 843.3 (3/ = 0
CX = – 800 N = 800 N 
Now use the x and y-direction Equations of Equilibrium:
FBD of member BC
CX
CY
B
FAB
400 N
1 m
2 m
1 m
800 N m
1
3

## Slide 11: CONCEPT QUIZ
1. The figures show a frame and its FBDs. If an additional couple moment is applied at C, how will you change the FBD of member BC at B?
A) No change, still just one force (FAB) at B. B) Will have two forces, BX and BY, at B. C) Will have two forces and a moment at B. D) Will add one moment at B.
Notes: Answer:
1. A

## Slide 12: CONCEPT QUIZ (continued)
2. The figures show a frame and its FBDs. If an additional force is applied at D, then how will you change the FBD of member BC at B?
A) No change, still just one force (FAB) at B. B) Will have two forces, BX and BY, at B. C) Will have two forces and a moment at B. D) Will add one moment at B.
 D
Notes: Answer:
2. B

## Slide 13: GROUP PROBLEM SOLVING
a) Draw FBDs of the frame’s members and pulleys.
b) Apply the equations of equilibrium and solve for the unknowns.
Given: The wall crane supports an external load of 700 lb.
Find: The force in the cable at winch motor W and the horizontal and vertical components of pin reactions at A, B, C, and D.
Plan:
Notes: Source : P6-74

## Slide 14: GROUP PROBLEM SOLVING (continued)
+  FY = 2 T – 700 = 0
T = 350 lb
FBD of the Pulley E
T
T
E
700 lb
Necessary Equations of Equilibrium:

## Slide 15: GROUP PROBLEM SOLVING (continued)
FBD of pulley C
C
350 lb
CY
CX
350 lb
FBD of pulley B
BY
BX
30°
350 lb
350 lb
B
+  FX = CX – 350 = 0 CX = 350 lb
+   FY = CY – 350 = 0 CY = 350 lb
+  FX = – BX + 350 – 350 sin 30° = 0 BX = 175 lb
 +  FY = BY – 350 cos 30° = 0 BY = 303.1 lb

## Slide 16: GROUP PROBLEM SOLVING (continued)
Please note that member BD is a two-force member.
+  MA = TBD sin 45° (4) – 303.1 (4) – 700 (8) = 0
TBD = 2409 lb
+  FY = AY + 2409 sin 45° – 303.1 – 700 = 0
AY = – 700 lb
+  FX = AX – 2409 cos 45° + 175 – 350 = 0
AX = 1880 lb
FBD of member ABC
AX
AY
A
45°
TBD
B
175 lb
303.11 lb
700 lb
350 lb
4 ft
4 ft

## Slide 17: GROUP PROBLEM SOLVING (continued)
At D, the X and Y component are
+ DX = –2409 cos 45° = –1700 lb
 + DY = 2409 sin 45° = 1700 lb
FBD of member BD
45°
B
2409 lb
D
DX
DY

## Slide 18: ATTENTION QUIZ
2. For the above problem, imagine that you have drawn a FBD of member BC. What will be the easiest way to write an equation involving unknowns at B?
A)  MC = 0 B)  MB = 0
C)  MA = 0 D)  FY = 0
1. When determining reactions at joints A, B and C, what is the minimum number of unknowns in solving this problem?
A) 6 B) 5
C) 4 D) 3
Notes: Answers:
1. D
2. A

## Slide 19
End of the Lecture
Let Learning Continue