## Slide 1: INTERNAL FORCES
In-Class Activities:
Check Homework
Reading Quiz
Applications
Types of Internal Forces
Steps for Determining
Internal Forces
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objective:
Students will be able to:
Use the method of sections for determining internal forces in 2-D load cases.

## Slide 2: READING QUIZ
1. In a multiforce member, the member is generally subjected to an internal _________.
A) Normal force B) Shear force
C) Bending moment D) All of the above.
2. In mechanics, the force component V acting tangent to, or along the face of, the section is called the _________ .
A) Axial force B) Shear force
C) Normal force D) Bending moment
Notes: Answers :
1. D
2. B

## Slide 3: APPLICATIONS
Why are the beams tapered? Internal forces are important in making such a design decision. In this lesson, you will learn about these forces and how to determine them.
Beams are structural members designed to support loads applied perpendicularly to their axes.
Beams can be used to support the span of bridges. They are often thicker at the supports than at the center of the span.

## Slide 4: APPLICATIONS (continued)
Usually such columns are wider/thicker at the bottom than at the top. Why?
A fixed column supports these rectangular billboards.

## Slide 5: APPLICATIONS (continued)
Why might have this been done?
The shop crane is used to move heavy machine tools around the shop.
The picture shows that an additional frame around the joint is added.

## Slide 6: INTERNAL FORCES
Then we need to cut the beam at B and draw a FBD of one of the halves of the beam. This FBD will include the internal forces acting at B. Finally, we need to solve for these unknowns using the E-of-E.
For example, we want to determine the internal forces acting on the cross section at B. But, first, we first need to determine the support reactions.
B
The design of any structural member requires finding the forces acting within the member to make sure the material can resist those loads.
B

## Slide 7: INTERNAL FORCES (continued)
The loads on the left and right sides of the section at B are equal in magnitude but opposite in direction. This is because when the two sides are reconnected, the net loads are zero at the section.
In two-dimensional cases, typical internal
loads are normal or axial forces (N, acting perpendicular to the section), shear forces (V, acting along the surface), and the bending moment (M).

## Slide 8: STEPS FOR DETERMINING INTERNAL FORCES
1. Take an imaginary cut at the place where you need to determine the internal forces. Then, decide which resulting section or piece will be easier to analyze.
2. If necessary, determine any support reactions or joint forces you need by drawing a FBD of the entire structure and solving for the unknown reactions.
3. Draw a FBD of the piece of the structure you’ve decided to analyze. Remember to show the N, V, and M loads at the “cut” surface.
4. Apply the E-of-E to the FBD (drawn in step 3) and solve for the unknown internal loads.

## Slide 9: EXAMPLE
Solution
Plan on taking the imaginary cut at C. It will be easier to work with the right section (from the cut at C to point B) since the geometry is simpler and there are no external loads.
Given: The loading on the beam.
Find: The internal forces at point C.
Plan: Follow the procedure!!
Notes: Source : F7-3

## Slide 10: EXAMPLE (continued)
Applying the E-of-E to this FBD, we get
 +  Fx = Bx = 0;
+  MA = − By ( 9 ) + 18 ( 3 ) = 0 ; By = 6 kip
2. We need to determine By. Use a FBD of the entire frame and solve the E-of-E for By.
Bx
3 ft
9 ft
Ay
By
18 kip
3 ft
FBD of the entire beam:

## Slide 11: EXAMPLE (continued)
3. Now draw a FBD of the right section. Assume directions for VC, NC and MC.
6 kip
VC
MC
NC
4.5 ft
C
B
4. Applying the E-of-E to this FBD, we get
 +  Fx = NC = 0; NC = 0
 +  Fy = – VC – 6 = 0; VC = – 6 kip
+  MC = – 6 (4.5) – MC = 0 ; MC = – 27 kip ft

## Slide 12: CONCEPT QUIZ
1. A column is loaded with a vertical 100 N force. At which sections are the internal loads the same?
A) P, Q, and R B) P and Q
C) Q and R D) None of the above.
•
P
Q
R
100 N
2. A column is loaded with a horizontal 100 N force. At which section are the internal loads largest?
A) P B) Q
C) R D) S
P
Q
R
100 N
S
Notes: Answers :
1.C
2.D

## Slide 13: GROUP PROBLEM SOLVING I
Given: The loading on the beam.
Find: The internal forces at point C.
Plan: Follow the procedure!!
Solution:
1. Plan on taking the imaginary cut at C. It will be easier to work with the left section (point A to the cut at C) since the geometry is simpler.
Notes: Source : P7-23

## Slide 14: GROUP PROBLEM SOLVING I (continued)
2. First, we need to determine Ax and Ay using a FBD of the entire frame.
Applying the E-of-E to this FBD, we get
 +  Fx = Ax + 400 = 0 ; Ax = – 400 N
+  MB = – Ay(5) – 400 (1.2) = 0 ; Ay = – 96 N
400 N
By
Ax
Ay
Free Body Diagram

## Slide 15: GROUP PROBLEM SOLVING I (continued)
3. Now draw a FBD of the left section. Assume directions for VC, NC and MC as shown.
4. Applying the E-of-E to this FBD, we get
 +  Fx = NC – 400 = 0; NC = 400 N
 +  Fy = – VC – 96 = 0; VC = – 96N
+  MC = 96 (1.5) + MC = 0 ; MC = -144 N m
96 N
VC
MC
NC
1.5 m
A
400 N
C

## Slide 16: GROUP PROBLEM SOLVING II
Solution:
1. Make an imaginary cut at C. Why there?
Which section will you pick to analyze via the FBD?
Given: The loading on the beam.
Find: The internal forces at point C.
Plan: Follow the procedure!!
Why will it be easier to work with segment AC?
Notes: Source : P7-19

## Slide 17: GROUP PROBLEM SOLVING II (continued)
+  MA = T ( 2.5 ) − 1800 (6) = 0 ; T = 4320 lb
 +  Fx = Ax − 4320 = 0 ; Ax = 4320 lb
 +  Fy = Ay − 1800 = 0 ; Ay = 1800 lb
2. Determine the reactions at A, using a FBD and the E-of-E for the entire frame.
T
Ax
Ay
1800 lb
6 ft
Free Body Diagram

## Slide 18: GROUP PROBLEM SOLVING II (continued)
3. A FBD of section AC is shown below.
VC
MC
NC
1.5 ft
A
C
450 lb
1.5 ft
FBD of Section AC
4320 lb
1800 lb
4. Applying the E-of-E to the FBD, we get
 +  Fx = NC + 4320 = 0 ; NC = – 4320 lb
 +  Fy = 1800 – 450 – VC = 0 ; VC = 1350 lb
+  MC = – 1800 (3) + 450 (1.5) + MC = 0 ; MC = 4725 lbft

## Slide 19: ATTENTION QUIZ
2. A column is loaded with a horizontal 100 N force. At which section are the internal loads the lowest?
A) P B) Q
C) R D) S
P
Q
R
100N
S
1. Determine the magnitude of the internal loads
(normal, shear, and bending moment) at point C.
A) (100 N, 80 N, 80 N m)
B) (100 N, 80 N, 40 N m)
C) (80 N, 100 N, 40 N m)
D) (80 N, 100 N, 0 N m )
•
C
0.5m
1 m
80 N
100 N
Notes: Answers:
1. B
2. A

## Slide 20
End of the Lecture
Let Learning Continue