## Slide 1: CHARACTERISTICS OF DRY FRICTION & PROBLEMS INVOLVING DRY FRICTION
In-Class Activities:
Check Homework, if any
Reading Quiz
Applications
Characteristics of Dry Friction
Problems involving Dry Friction
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objective:
Students will be able to:
a) Understand the characteristics of dry friction
b) Draw a FBD including friction.
c) Solve problems involving friction.

## Slide 2: READING QUIZ
1. A friction force always acts _____ to the contact surface.
  A) Normal B) At 45°
  C) Parallel D) At the angle of static friction
2. If a block is stationary, then the friction force acting on it is ________ .
  A)  s N B) = s N
  C)  s N D) = k N
Notes: Answers:
1. C
2. A

## Slide 3: APPLICATIONS
For an applied force on the bike tire brake pads, how can we determine the magnitude and direction of the resulting friction force?
In designing a brake system for a bicycle, car, or any other vehicle, it is important to understand the frictional forces involved.

## Slide 4: APPLICATIONS (continued)
What physical factors affect the answer to this question?
The rope is used to tow the refrigerator.
In order to move the refrigerator, is it best to pull up as shown, pull horizontally, or pull downwards on the rope?

## Slide 5: CHARACTERISTICS OF DRY FRICTION (Section 8.1)
Friction is defined as a force of resistance acting on a body which prevents or resists the slipping of a body relative to a second body.
Experiments show that frictional forces act tangent (parallel) to the contacting surface in a direction opposing the relative motion or tendency for motion.
For the body shown in the figure to be in equilibrium, the following must be true: F = P, N = W, and W*x = P*h.

## Slide 6: CHARACTERISTICS OF DRY FRICTION (continued)
To study the characteristics of the friction force F, let us assume that tipping does not occur (i.e., “h” is small or “a” is large).
Then we gradually increase the magnitude of the force P.
Typically, experiments show that the friction force F varies with P, as shown in the right figure above.

## Slide 7: CHARACTERISTICS OF DRY FRICTION (continued)
The maximum friction force is attained just before the block begins to move (a situation that is called “impending motion”). The value of the force is found using Fs = s N, where s is called the coefficient of static friction. The value of s depends on the two materials in contact.
Once the block begins to move, the frictional force typically drops and is given by Fk = k N. The value of k (coefficient of kinetic friction) is less than s .

## Slide 8: CHARACTERISTICS OF DRY FRICTION (continued)
It is also very important to note that the friction force may be less than the maximum friction force. So, just because the object is not moving, don’t assume the friction force is at its maximum of Fs = s N unless you are told or know motion is impending!

## Slide 9: DETERMING s EXPERIMENTALLY
If the block just begins to slip, the maximum friction force is Fs = s N, where s is the coefficient of static friction.
Thus, when the block is on the verge of sliding, the normal force N and
frictional force Fs combine to create a resultant Rs.
From the figure,
tan s = ( Fs / N ) = (s N / N ) = s

## Slide 10: DETERMING s EXPERIMENTALLY (continued)
Using these two equations, we get s = (W sin s ) / (W cos s ) = tan s This simple experiment allows us to find the S between two materials in contact.
A block with weight w is placed on an inclined plane. The plane is slowly tilted until the block just begins to slip.
The inclination, s, is noted. Analysis of the block just before it begins to move gives (using Fs = s N):
+  Fy = N – W cos s = 0
+  FX = S N – W sin s = 0

## Slide 11: PROBLEMS INVOLVING DRY FRICTION (Section 8.2)
Steps for solving equilibrium problems involving dry friction:
1. Draw necessary free body diagrams. Make sure that you show the friction force in the correct direction (it always opposes the motion or impending motion).
2. Determine the number of unknowns. Do not assume that F = S N unless the impending motion condition is given.
3. Apply the equations of equilibrium and appropriate frictional equations to solve for the unknowns.

## Slide 12: IMPENDING TIPPING versus SLIPPING
Hence, we have to make an assumption to give us another equation (the friction equation!). Then we can solve for the unknowns using the three E-of-E. Finally, we need to check if our assumption was correct.
For a given W and h of the box, how can we determine if the block will slide or tip first? In this case, we have four unknowns (F, N, x, and P) and only the three E-of-E.

## Slide 13: IMPENDING TIPPING versus SLIPPING (continued)
Assume: Slipping occurs
Known: F = s N
Solve: x, P, and N
Check: 0  x  b/2
Or
Assume: Tipping occurs
Known: x = b/2
Solve: P, N, and F
Check: F  s N

## Slide 14: EXAMPLE
a) Draw a FBD of the box.
b) Determine the unknowns.
c) Make your friction assumptions.
d) Apply E-of-E (and friction equations, if appropriate ) to solve for the unknowns.
e) Check assumptions, if required.
Given: Crate weight = 250 lb and s = 0.4
Find: The maximum force P that can be applied without causing movement of the crate.
Plan:
??
Notes: Source : F8-5

## Slide 15: EXAMPLE (continued)
x
1.5 ft
1.5 ft
250 lb
0
F
FBD of the crate
P
N
3.5 ft
4.5 ft
There are four unknowns: P, N, F and x.
First, let’s assume the crate slips. Then the friction equation is F = s N = 0.4 N.
Solution:

## Slide 16: EXAMPLE (continued)
+   FX = P – 0.4 N = 0
+   FY = N – 250 = 0
Solving these two equations gives:
P = 100 lb and N = 250 lb
+  MO = -100 (4.5) + 250 (x) = 0
Check: x = 1.8  1.5 : No slipping will occur since x  1.5
x
1.5 ft
1.5 ft
250 lb
0
F
FBD of the crate
P
N
3.5 ft
4.5 ft

## Slide 17: EXAMPLE (continued)
+   FX = P – F = 0
+   FY = N – 250 = 0
These two equations give:
P = F and N = 250 lb
+ MO = – P (4.5) + 250 (1.5) = 0
P = 83.3 lb, and F = 83.3 lb  s N = 100 lb
Since tipping occurs, here is the correct FBD:
1.5 ft
1.5 ft
250 lb
0
F
FBD of the crate
P
N
3.5 ft
4.5 ft

## Slide 18: CONCEPT QUIZ
1. A 100 lb box with a wide base is pulled by a force P and s = 0.4. Which force orientation requires the least force to begin sliding?
A) P(A) B) P(B)
C) P(C) D) Can not be determined
P(A)
P(B)
P(C)
100 lb
2. A ladder is positioned as shown. Please indicate the direction of the friction force on the ladder at B.
A)  B) 
C) D)
A
B
Notes: Answer:
1. A
2. C

## Slide 19: GROUP PROBLEM SOLVING
a) Draw FBDs of the car.
b) Determine the unknowns.
d) Apply the E-of-E and friction equations to solve for the unknowns.
Given: Automobile has a mass of 2000 kg and s = 0.3.
Find: The smallest magnitude of F required to move the car if the back brakes are locked and the front wheels are free to roll.
Plan:
Notes: Source : P8-5

## Slide 20: GROUP PROBLEM SOLVING (continued)
Assume that the rear wheels are on the verge of slip. Thus
FB = µs NB = 0.3 NB (4)
FBD of the car
NA
NB
FB
2000 × 9.81 N
+   FX = FB – F (cos 30) = 0 (1)
+   FY = NA + NB + F (sin 30) – 19620 = 0 (2)
+  MA = F cos30(0.3) – F sin30(0.75) + NB (2.5) – 19620(1) = 0 (3)
Note that there are four unknowns: F, NA, NB, and FB.
Here is the correct FBD:
Equations of Equilibrium:

## Slide 21: GROUP PROBLEM SOLVING (continued)
Solving Equations (1) to (4),
F = 2763 N
and NA =10263 N, NB = 7975 N, FB = 2393 N.

## Slide 22: ATTENTION QUIZ
1. A 10 lb block is in equilibrium. What is the magnitude of the friction force between this block and the surface?
A) 0 lb B) 1 lb
C) 2 lb D) 3 lb
 S = 0.3
2 lb
2. The ladder AB is positioned as shown. What is the direction of the friction force on the ladder at B.
A) B)
C)  D) 
A
B
Notes: Answers are:
1. C
2. D

## Slide 23
End of the Lecture
Let Learning Continue